CORRIGENDUM No: 1

to the

TENDER DOSSIER-ANNEX II + III: TECHNICAL SPECIFICATIONS + TECHNICAL OFFER

Publication Ref: 2007CB16IPO006-2011-2-26-001 PP1/LP

TED/E-notice Contract notice reference: 2014/S 039-065363

# Subject: Procurement of speciality vehicle: Mobile Internet Research and Training Unit for the EU-funded Bulgaria-Serbia IPA CBC project: Mobile internet, e-services and training for rural community in cross-border region – E-Inclusion

Location – Leskovac, Republic of Serbia

The following corrections are made to the ANNEX II + III: TECHNICAL SPECIFICATIONS + TECHNICAL OFFER:

The former text:

| 1. Item Number | 2. Specifications Required | 3. Specifications Offered | 4. Notes, remarks, ref to documentation | 5. Evaluation Committee’s notes |
| --- | --- | --- | --- | --- |
| 1 | Chassis Cab ~5 tones weight; Engine: Min 2,0-max 2,5 litre Diesel - 4 cylinder – min 80-max120 Kw; Gearbox: 6 Speed + reverse; Breaks ABS with EDB; ESP Stability Control; Emissions level: Min Euro 5 Exterior: Halogen Headlamps with Load Height Adjustment; Electric Operated Front Windows; Remote Electric Central Locking; Rear Visibility Camera, Parking Sensor with Buzzer, Front fog lights. Interior: Air-conditioning; Power Steering; Cruise Control; 2 Air Bags; Head Restraints; Height Adjustable Steering Wheel; Digital Tachograph; Radio with CD; 3 Point Seat Belts (pre- tensioned); Alarm; Colour: White Speedometer in km/h, left steering wheel. |  |  |  |

Shall read as new text:

| 1. Item Number | 2. Specifications Required | 3. Specifications Offered | 4. Notes, remarks, ref to documentation | 5. Evaluation Committee’s notes |
| --- | --- | --- | --- | --- |
| 1 | Chassis Cab 5 tones weight (± 5%). Engine: Min 2,0-max 2,5 litre Diesel - 4 cylinder – min 80-max120 Kw; Gearbox: 6 Speed + reverse; Breaks ABS with EDB; ESP Stability Control; Emissions level: Min Euro 5 Exterior: Halogen Headlamps with Load Height Adjustment; Electric Operated Front Windows; Remote Electric Central Locking; Rear Visibility Camera, Parking Sensor with Buzzer, Front fog lights. Interior: Air-conditioning; Power Steering; Cruise Control; 2 Air Bags; Head Restraints; Height Adjustable Steering Wheel; Digital Tachograph; Radio with CD; 3 Point Seat Belts (pre- tensioned); Alarm; Colour: White Speedometer in km/h, left steering wheel. |  |  |  |

All other terms and conditions of the Tender Dossier remain unchanged. The above corrections to the ANNEX II + III: TECHNICAL SPECIFICATIONS + TECHNICAL OFFER are integral part of the ANNEX II + III: TECHNICAL SPECIFICATIONS + TECHNICAL OFFER and Tender Dossier.